ROS Enhancement Proposals (REPs)
For more details see: REP 103 and REP 105
Reference:
REP 103 Axis Orientation
X axis is indicated in red
Y axis is indicated in green
Z axis is indicated in blue
Chirality
All systems are right handed. This means they comply with the right hand rule
For right-handed coordinates your right thumb points along the Z axis in a positive Z-direction and the curl of your fingers represents a motion from the first or X axis to the second or Y axis. When viewed from the top or Z axis the system is counter-clockwise.
By the right hand rule, the yaw component of orientation increases as the child frame rotates counter-clockwise, and for geographic poses, yaw is zero when pointing east.
This requires special mention only because it differs from a traditional compass bearing, which is zero when pointing north and increments clockwise. Hardware drivers should make the appropriate transformations before publishing standard ROS messages.
up
left
up
forward
BASE_LINK
north
In relation to a body the standard is:
    x forward
    y left
    z up
geographic locations (ENU) convention:
    X east
    Y north
    Z up
east
MAP

---
navsat_transform_node takes as input a nav_msgs/Odometry message, a sensor_msgs/Imu containing an accurate estimate of your robot’s heading, and a sensor_msgs/NavSatFix message containing GPS data. It produces an odometry message in coordinates that are consistent with your robot’s world frame. This value can be directly fused into your state estimate. Publishes world_frame->utm transform
utm_odometry_node (aka gps_conv) converts latitude-longitude readings into UTM odometry
ekf_localization_node is an implementation of an extended Kalman filter. It uses an omnidirectional motion model to project the state forward in time, and corrects that projected estimate using perceived sensor data.
a 0 heading corresponds to east. Check yaw_offset: 0.0 in navsat_transform. navsat_transform_node launched by
dual_ekfnavsat.

---
4.2.3 Orientation data
The MTi calculates the orientation (DataID 0x2010, 0x2020, 0x2030) between the calibrated inertial data and magnetic field, represented in (S) or (O), and the local Earth-fixed coordinate system (L).
By default the local earth-fixed reference co-ordinate system used is defined as a right handed Cartesian co-ordinate system with:
X positive to the East (E).
Y positive to the North (N).
Z positive when pointing up (U).
This coordinate system is known as ENU and is the standard in inertial navigation for aviation and geodetic applications. Note that it is possible to change the coordinate system using an alignment matrix or orientation reset.
The 3D orientation output is defined as the orientation between the body-fixed co-ordinate system, (S), and the earth-fixed co-ordinate system, (L), using the earth-fixed co-ordinate system, (L), as the reference co-ordinate system.
Interpretation of yaw as heading3
Heading is defined as the angle between north and horizontal projection of the vehicle roll axis. Yaw is defined for a particular local-level navigation frame as the angle from a horizontal navigation axis to the projection of the longitudinal axis in the horizontal plane following the right-hand rule. Based on the definition of heading and yaw, consider the use of the MTi in an aircraft which is stationary and pointing north. Below, a table is displayed that shows the heading and yaw outputs for the three reference coordinate system (available with MTi)
Similarly if you would like to use the ENU as your local frame, mount the MTi such that the y-axis is pointing to the direction of motion of the vehicle. In section 4.11 the various alignment resets are described.
sensor-fixed output coordinate system (S)
object coordinate system (O)
local Earth-fixed coordinate system (L)

---
If the CNS-5000 is not mounted precisely with the Z-axis pointing
up and the Y-axis pointing forward along the direction of travel,
you will need to enter additional configuration commands prior
to use.
To configure the CNS-5000 for proper operation, you will need to
enter the offset distances between the phase center of the GNSS
antenna and each axis of the CNS-5000 (also called the “lever arm
offset”).